HAPI Support Documentation
Document Name: RTU Installation and Configuration
Version: 1.0, June 24th 2016
Author(s): Tyler Reed
Note: This document assumes the user has a workstation for working with Arduino hardware
# RTU 2017
The RTU code in the firmware directory supports multiple configurations in one source location. Change the #ifdef at the beginning to enable ENET, USB or NodeMCU configurations. The current firmware works with the September 2016 master controller, but has not been verified against the April2017 programs. The format of the database has changed.
Note that the firmware includes the following defaults:
- RTU0xx	Mega2560 ENET
- RTU1xx	Mega2560 USB
- RTU2xx	UNO USB
- RTU3xx	NodeMCU/ESP8266
Configuration of the RTU pins is done by editing the load_pins.sql file before running create_database.sql
Sample files have been uploaded for Mega2560, UNO and NodeMCU. This change should also be made in the create_database.sql file.

# Remote Terminal Unit Installation Procedure
Step	Description	Location/Command
1	Install the latest Arduino IDE on workstation	https://www.arduino.cc/en/Main/Software
2	Get the lastest RTU code from HAPI github repository	git clone https://github.com/mayaculpa/hapi.git
3	Load the appropriate sketch in the IDE	E.g. arduino_mega2560_enet.ino
4	Modify the mac address by incrementing the last byte by 1 for each RTU in the local environment.
5	Make custom code changes as necessary	Yeah, not to helpful, I know.
6	Upload the sketch to the RTU
7	Position RTU in growing environment and connect sensors as necessary	Even less helpful
8	Connect RTU to Ethernet
9	Power on the RTU